## Slide 1: Advanced Computer Networks
TCP and Fair Queuing

## Slide 2: Introduction to TCP
Communication abstraction:
  Reliable
  Ordered
  Point-to-point
  Byte-stream
  Full duplex
  Flow and congestion controlled
Protocol implemented entirely at the ends
  Fate sharing
Sliding window with cumulative acks
  Ack field contains last in-order packet received
  Duplicate acks sent when out-of-order packet received

## Slide 3: Key Things You Should Know Already
Port numbers
TCP/UDP checksum
Sliding window flow control
  Sequence numbers
TCP connection setup
TCP reliability
  Timeout
  Data-driven

## Slide 4: TCP Congestion Control
Changes to TCP motivated by ARPANET congestion collapse
Basic principles
  Additive increase/multiplicative decrease (AIMD)
  Packet conservation
  Reaching steady state quickly
  ACK clocking

## Slide 5: TCP Congestion Control - Solutions
Reaching equilibrium
  Slow start
Eliminates spurious retransmissions
  Accurate RTO estimation
  Fast retransmit
Adapting to resource availability
  Congestion avoidance
Notes: ACK
1
2
3
3
3

## Slide 6: AIMD
Distributed, fair and efficient
Packet loss is seen as sign of congestion and results in a multiplicative rate decrease
  Factor of 2
TCP periodically probes for available bandwidth by increasing its rate
Time
Rate
Notes: Half: someone else may just start to use the BW
Implementation Issue
Operating system timers are very coarse – how to pace packets out smoothly?
Implemented using a congestion window that limits how much data can be in the network.
  TCP also keeps track of how much data is in transit
Data can only be sent when the amount of outstanding data is less than the congestion window.
  The amount of outstanding data is increased on a “send” and decreased on “ack”
  (last sent – last acked) < congestion window
Window limited by both congestion and buffering
  Sender’s maximum window = Min (advertised window, cwnd)

## Slide 7: Congestion Avoidance
If loss occurs when cwnd = W
  Network can handle 0.5W ~ W segments
  Set cwnd to 0.5W (multiplicative decrease)
Upon receiving ACK
  Increase cwnd by (1 packet)/cwnd
    What is 1 packet?  1 MSS worth of bytes
    After cwnd packets have passed by  approximately increase of 1 MSS
Implements AIMD
Notes: MSS: Maximum Segment Size
BW=cwnd/RTT, very rough calculation

## Slide 8: Congestion Avoidance Behavior
Time
Congestion
Window
Packet loss
+ Timeout
Grabbing
back
Bandwidth
Cut
Congestion
Window
and Rate

## Slide 9: Packet Conservation
At equilibrium, inject packet into network only when one is removed
  Sliding window and not rate controlled
  But still need to avoid sending burst of packets  would overflow links
    Need to carefully pace out packets
    Helps provide stability
Need to eliminate spurious retransmissions
  Accurate RTO estimation
  Better loss recovery techniques (e.g. fast retransmit)
Notes: Spurious: retransmit the same pkt which is already on the way to Dest.
Goodput=1-loss, not as worse as before

## Slide 10: TCP Packet Pacing
Congestion window helps to “pace” the transmission of data packets
In steady state, a packet is sent when an ack is received
  Data transmission remains smooth, once it is smooth
  Self-clocking behavior
Pr
Pb
Ar
Ab
Receiver
Sender
As
Notes: Space is a reflection of the slowest link on the route
Self-clocking: send as the pace of the slowest link handle

## Slide 11: Reaching Steady State
Doing AIMD is fine in steady state but slow…
How does TCP know what is a good initial rate to start with?
  Should work both for a CDPD (10s of Kbps or less) and for supercomputer links (10 Gbps and growing)
Quick initial phase to help get up to speed (slow start)
Notes: Cellular Digital Packet Data (CDPD)
100Mbps link, RTT=100ms
10Mb data
~1MB pkt, for 1Kb pkt size  Cwnd =1k, increase 1 per RTT, will take for ever.

## Slide 12: Slow Start Packet Pacing
How do we get this clocking behavior to start?
  Initialize cwnd = 1
  Upon receipt of every ack, cwnd = cwnd + 1
Implications
  Window actually increases to W in RTT * log2(W)
  Can overshoot window and cause packet loss
Notes: Quick way to figure out your fair share?
Remember the overshoot, next time half it.
Double cwnd every RTT
Used in TCP to get rough estimate of network and establish ack clock
  Don’t need it for ack clock
  TCP ensures that overshoot is not > 2x
  Rate based protocols have no such limitation – why?

## Slide 13: Slow Start Example
1
One RTT
One pkt time
0R
2
1R
3
4
2R
5
6
7
8
3R
9
10
11
12
13
14
15
1
2
3
4
5
6
7

## Slide 14: Return to Slow Start
If packet is lost we lose our self clocking as well
  Need to implement slow-start and congestion avoidance together
When timeout occurs set ssthresh to 0.5w
  If cwnd < ssthresh, use slow start
  Else use congestion avoidance

## Slide 15: TCP Saw Tooth Behavior
Time
Congestion
Window
Initial
Slowstart
Fast
Retransmit
and Recovery
Slowstart
to pace
packets
Timeouts
may still
occur
Notes: Slow start, overshoot,
Restart slow start, with better idea of the network

## Slide 16: Changing Workloads
New applications are changing the way TCP is used
1980’s Internet
  Telnet & FTP  long lived flows
  Well behaved end hosts
  Homogenous end host capabilities
  Simple symmetric routing
2000’s Internet
  Web & more Web  large number of short xfers
  Wild west – everyone is playing games to get bandwidth
  Cell phones and toasters on the Internet
  Policy routing
How to accommodate new applications?
Notes: How to set multi-media stream BW (or cWnd)?

## Slide 17: TCP Friendliness
What does it mean to be TCP friendly?
  TCP is not going away
  Any new congestion control must compete with TCP flows
    Should not clobber TCP flows and grab bulk of link
    Should also be able to hold its own, i.e. grab its fair share, or it will never become popular
How is this quantified/shown?
  Has evolved into evaluating loss/throughput behavior
  If it shows 1/sqrt(p) behavior it is ok
Notes:   But is this really true?

## Slide 18: TCP Friendly Rate Control (TFRC)
Equation 1 – real TCP response
  1st term corresponds to simple derivation
  2nd term corresponds to more complicated timeout behavior
    Is critical in situations with > 5% loss rates  where timeouts occur frequently
Key parameters
  RTO
  RTT
  Loss rate

## Slide 19: TCP Performance
Can TCP saturate a link?
Congestion control
  Increase utilization until… link becomes congested
  React by decreasing window by 50%
  Window is proportional to rate * RTT
Doesn’t this mean that the network oscillates between 50 and 100% utilization?
  Average utilization = 75%??
  No…this is *not* right!
Notes: How fast TCP goes?
TCP in local can get 90Mbps out of 100Mbps link, how come?
Not right, because
BW=cWnd/RTT, RTT not a constant due to queue

## Slide 20: TCP Congestion Control
Only W packets may be outstanding
Rule for adjusting W
  If an ACK is received: W ← W+1/W
  If a packet is lost: W ← W/2
Source
Dest
t
Window size

## Slide 21: Single TCP Flow Router without buffers

## Slide 22: Summary Unbuffered Link
t
W
Minimum window for full utilization
The router can’t fully utilize the link
  If the window is too small, link is not full
  If the link is full, next window increase causes drop
  With no buffer it still achieves 75% utilization

## Slide 23: TCP Performance
In the real world, router queues play important role
  Window is proportional to rate * RTT
    But, RTT changes as well the window
  Window to fill links = propagation RTT * bottleneck bandwidth
    If window is larger, packets sit in queue on bottleneck link
Notes: Why Router needs Queue?
Avoid loss, congestion,
Increase link utilization
Downside: large delay, managing queue no easy

## Slide 24: Single TCP Flow Router with large enough buffers for full link utilization
Notes:     To use the outgoing link at full speed, or utilization=100%, half pkts on the wire (BW*RTT), half in queue.

## Slide 25: TCP Performance with Queue
If we have a large router queue  can get 100% utilization
  But, router queues can cause large delays
How big does the queue need to be?
  Windows vary from W  W/2
    Must make sure that link is always full
    W/2 > RTT * BW
    W = RTT * BW + Qsize
    Therefore, Qsize > RTT * BW
  Ensures 100% utilization
  Delay?
    Varies between RTT and 2 * RTT

## Slide 26: Summary Buffered Link
t
W
Minimum window for full utilization
With sufficient buffering we achieve full link utilization
  The window is always above the critical threshold
  Buffer absorbs changes in window size
    Buffer Size = Height of TCP Sawtooth
    Minimum buffer size needed is 2T*C, where T=RTT, C=BW
  This is the origin of the rule-of-thumb
Buffer
Notes: Saw height: W/2
W/2 >= outgoing pkts=RTT*BW
W>= 2*RTT*BW

## Slide 27: Queuing Disciplines
Each router must implement some queuing discipline
Queuing allocates both bandwidth and buffer space:
  Bandwidth: which packet to serve (transmit) next
  Buffer space: which packet to drop next (when required)
Queuing also affects latency

## Slide 28: Typical Internet Queuing
FIFO + drop-tail
  Simplest choice
  Used widely in the Internet
FIFO (first-in-first-out)
  Implies single class of traffic
Drop-tail
  Arriving packets get dropped when queue is full regardless of flow or importance
Important distinction:
  FIFO: scheduling discipline
  Drop-tail: drop policy